## Slide 1
CDM DATATHON-2026 · THEME 6.1 · CONTESTED AND CONGESTED
Project High Ground
The crowding of orbit, and what it means for India and the Indian Armed Forces
[Rank] Arjun Jayadev
[Service No] · [Unit / Formation]
College of Defence Management · 2026
Notes: Sir, my study takes the CDM satellite data and asks five questions: how crowded orbit has become, who owns it, how dangerous it is, who is building military eyes in it, and what India should do. About fifteen minutes, then questions.

## Slide 2
BOTTOM LINE UP FRONT
Orbit is crowded, concentrated and contested
15×
working satellites since 2014: 1,167 to 17,062
×10
collision-risk index in low orbit, against 2014
406 : 17
state ISR and military satellites, China : India
Decision sought: a four-month ORBITWATCH proof of concept at the Defence Space Agency, using the open catalogue and the pipeline already built.
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
2 / 17
Notes: Three numbers carry the study. Working satellites rose 15-fold in twelve years. Collision risk in low orbit is about ten times the 2014 level. And China operates about 406 state intelligence and military satellites to India's 17. India's share of working satellites has fallen to 0.5 percent. Everything that follows is the evidence, and at the end one decision.

## Slide 3
DEFINING THE PROBLEM · DATA
Five questions, seven sources of evidence
How crowded has orbit become since 2014?
Whose satellites are they, and what are they for?
Where is orbit crowded, and how dangerous is it?
Who is building military eyes in orbit?
What should India and its Armed Forces do?
CDM satellite census
1,167 active satellites, Jan 2014
CDM space weather
139,872 hours of Dst + sunspots
CDM MODIS fires
1.25 million detections, 2010-20
Satellite catalogue (open)
70,366 objects to 21 Sep 2026
UCS 2020 + UNOOSA (open)
second census; launches by country
Official and news
ISRO, PIB, ESA, NOAA, 2024-26
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
3 / 17
Notes: The theme asks for insights into satellite proliferation and a prediction of the trajectory. I turned that into five questions a commander would ask. The CDM data give the 2014 baseline, space weather and a real example of what satellites see. The open catalogue brings the picture to September 2026. Every number is regenerated from raw data by one command.

## Slide 4
FINDING 1 · THE CROWD
15 times more working satellites in twelve years
Chart: Working satellites, three censuses
| Jan 2014 (CDM) | Apr 2020 (UCS) | Sep 2026 (catalogue)
Working satellites | 1167 | 2666 | 17062
Chart: Satellites launched per year (2026 to 21 Sep)
| 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Other satellites | 117 | 123 | 126 | 199 | 189 | 172 | 174 | 390 | 400 | 330 | 396 | 775 | 697 | 876 | 823 | 1311 | 1089
Starlink | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 120 | 833 | 989 | 1690 | 1984 | 1964 | 3169 | 2141
Growth changed gear in 2021: 4% a year before, 47% after. One constellation now holds 65% of working satellites.
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
4 / 17
Notes: Three independent counts: the CDM census of 2014, the UCS database of 2020, and today's catalogue. From 1,167 to 17,062. A change-point test puts the break around 2021, when the mega-constellations began. Satellites launched a year went from 199 in 2013 to 4,480 in 2025. UN registrations match the catalogue almost exactly, so the count is sound.

## Slide 5
FINDING 2 · WHO OWNS ORBIT
One country and one company own most of orbit
Chart: Share of working satellites by country (%)
| USA | China | Russia | UK | Japan | India
Jan 2014 | 43 | 10 | 10.1 | 2.1 | 3.7 | 2.8
Sep 2026 | 76 | 9 | 2.2 | 4.1 | 0.9 | 0.5
76%
of working satellites are US-operated (43% in 2014)
5,879
concentration index (HHI); above 2,500 = highly concentrated. 2014: 2,171
0.5%
India's share: 33 satellites (2.8%) in 2014, 78 today
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
5 / 17
Notes: Control of orbit is concentrating. The USA went from 43 to 76 percent of working satellites, mostly one company. China grew thirteen-fold in numbers but held its share near ten percent. India grew from 33 to 78 satellites, but its share fell from 2.8 to 0.5 percent. The concentration index is more than double the 'highly concentrated' threshold.

## Slide 6
FINDING 3 · WHERE IT IS CROWDED
A live crowd, a dead crowd, and collision risk ×10
Chart: Objects in low orbit by altitude (km, 25 km shells), Sep 2026
| 200 | 225 | 250 | 275 | 300 | 325 | 350 | 375 | 400 | 425 | 450 | 475 | 500 | 525 | 550 | 575 | 600 | 625 | 650 | 675 | 700 | 725 | 750 | 775 | 800 | 825 | 850 | 875 | 900 | 925 | 950 | 975 | 1000 | 1025 | 1050 | 1075 | 1100 | 1125 | 1150 | 1175 | 1200 | 1225 | 1250 | 1275 | 1300 | 1325 | 1350 | 1375 | 1400 | 1425 | 1450 | 1475
Working satellites | 6 | 10 | 54 | 23 | 82 | 187 | 753 | 99 | 272 | 275 | 5979 | 3843 | 523 | 457 | 556 | 504 | 170 | 443 | 54 | 83 | 23 | 23 | 29 | 125 | 54 | 30 | 18 | 44 | 47 | 55 | 51 | 15 | 2 | 20 | 201 | 42 | 30 | 128 | 65 | 318 | 336 | 2 | 0 | 0 | 1 | 3 | 0 | 0 | 26 | 3 | 0 | 59
Debris | 0 | 1 | 1 | 6 | 2 | 4 | 6 | 10 | 14 | 24 | 28 | 33 | 52 | 67 | 92 | 131 | 159 | 223 | 263 | 377 | 424 | 494 | 583 | 656 | 692 | 670 | 645 | 510 | 371 | 320 | 285 | 282 | 201 | 181 | 143 | 133 | 125 | 114 | 85 | 73 | 64 | 59 | 165 | 129 | 49 | 61 | 58 | 51 | 59 | 67 | 68 | 109
Dead satellites and rocket bodies | 3 | 3 | 2 | 6 | 9 | 11 | 16 | 18 | 19 | 27 | 45 | 36 | 31 | 46 | 56 | 53 | 98 | 49 | 44 | 56 | 55 | 59 | 151 | 124 | 61 | 85 | 69 | 37 | 50 | 62 | 113 | 261 | 25 | 21 | 21 | 41 | 20 | 9 | 10 | 29 | 6 | 6 | 1 | 4 | 7 | 19 | 6 | 35 | 143 | 138 | 134 | 103
9,964
objects at 450-500 km, 99% working (425 in 2014)
4,583
objects at 750-900 km, 82% of them debris
162
GEO satellites in India's 40-110 E arc, 29% of the belt
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
6 / 17
Notes: Orbit is crowded in two places. The live crowd at 450 to 500 kilometres, almost all working satellites. The dead crowd at 750 to 900 kilometres, mostly debris from the 2007 Chinese test and the 2009 collision. Collisions grow with the square of the number of objects at each height, so the collision-risk index is about 10 times its 2014 level. Higher up, the geostationary arc India uses holds 162 satellites; China and the USA each have more there than India.

## Slide 7
FINDING 4 · WEAPON TESTS
Altitude decides how long weapon debris stays
Chart: Share of catalogued debris still in orbit, Sep 2026 (%)
| China ASAT test (Jan 2007) | Iridium-Cosmos collision (Russian debris) (Feb 2009) | Iridium-Cosmos collision (US debris) (Feb 2009) | US ASAT intercept (Feb 2008) | India ASAT test (Mission Shakti) (Mar 2019) | Russia ASAT test (Nov 2021)
Still in orbit % | 65.5 | 35.8 | 17.8 | 0 | 0 | 0.2
Event | Pieces | Left
China ASAT test | 3,531 | 65.5%
Iridium-Cosmos collision (Russian debris) | 1,714 | 35.8%
Iridium-Cosmos collision (US debris) | 656 | 17.8%
US ASAT intercept | 174 | 0%
India ASAT test (Mission Shakti) | 129 | 0%
Russia ASAT test | 1,806 | 0.2%
India's 2019 test at ~280 km: all 129 pieces re-entered. China's 2007 test at ~865 km: 66% still in orbit after 20 years.
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
7 / 17
Notes: Six events, one lesson. China's 2007 test at high altitude made over three and a half thousand tracked pieces, and two thirds are still up nearly twenty years later. India's 2019 test was done low; every piece re-entered, most within half a year. Russia's 2021 test has almost cleared. A responsible test is a low one, and India can say so with data.

## Slide 8
FINDING 5 · THE CONTEST
China and the USA build eyes by the hundred
Chart: Military, state-ISR and imaging satellites working, Sep 2026 (name-based lower bound)
| USA | China | Russia | India | India + SBS-III (2029)
Operational | 542 | 406 | 146 | 17 | 69
43 a year
Chinese state-ISR satellites launched, 2023-25 average (India: under one)
13%
of today's China-India gap closed by SBS-III's 52 satellites (due 2029)
305
US national-security payloads launched since 2024
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
8 / 17
Notes: Grouping satellites by official programme names gives a transparent lower bound. China operates about 406, including 164 Yaogan reconnaissance satellites, and adds about 43 a year. India operates about 17. SBS-III is the right answer but closes only about 13% of today's gap. During Operation Sindoor ten Indian satellites worked round the clock: the need is proven, the capacity is thin.

## Slide 9
FINDING 6 · THE NATURAL ADVERSARY
Storm odds rise ~7-fold when the Sun is active
Chart: Intense storms per 30 days (CDM Dst data)
| <30 | 30-60 | 60-100 | >=100
Intense storms per 30 days | 0.06 | 0.39 | 0.5 | 0.59
Chart: Low-orbit debris re-entering per year (%): a 12-year cycle
39% vs 6%
chance of an intense storm in any 30 days, active vs quiet Sun. Storms killed 38 new Starlink satellites (Feb 2022); solar cycle 25 peaked in Oct 2024.
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
9 / 17
Notes: The Sun is the adversary nobody can deter. In the CDM records, when sunspots are high, the chance of an intense magnetic storm in a month is 39%; when quiet, 6%. A Poisson model gives 1.88 times the rate per 50 sunspots. A periodogram of debris re-entries finds a 12-year cycle on its own: the solar cycle heats the upper atmosphere and drags objects down.

## Slide 10
FINDING 7 · WHAT EYES IN ORBIT BUY
Two satellites saw what one would have missed
1.25 million fire and heat detections by NASA's Terra and Aqua over the USA, 2010-2020 (CDM data)
Chart: Who saw each fire-day (10 km grid)
| Aqua only | Terra only | Both
Fire-days | 45.5 | 38.5 | 16
84%
of fire-days seen by only one of the two satellites
21%
of detections at night: thermal sensors see in the dark
659
persistent industrial heat sources found (steel mills, smelters)
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
10 / 17
Notes: Why take all this risk? Because of what satellites see. Terra passes in the morning, Aqua in the afternoon. On a ten-kilometre grid, 84% of fire-days were seen by only one of them: a single satellite would have missed nearly half. For the Services the lesson is direct: persistence comes from numbers, and revisit decides whether a mobilisation or a launcher is caught in time.

## Slide 11
PREDICTION · THE TRAJECTORY TO 2030
About 31,000 working satellites by 2030
Chart: Satellites in orbit, 2000-2030
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
Payloads in orbit (catalogue) | 3145 | 3178 | 3228 | 3288 | 3340 | 3387 | 3455 | 3533 | 3614 | 3710 | 3790 | 3874 | 3966 | 4126 | 4227 | 4322 | 4427 | 4762 | 5050 | 5415 | 6528 | 8123 | 10146 | 12338 | 14042 | 17414 | 19971
Statistical trend (damped) | 19971 | 23257 | 26944 | 31178 | 36033
Chart: Collision-risk index, low orbit (2014 = 1)
| Jan 2014 | Sep 2026 | 2030 Low | 2030 Base | 2030 High
Index | 1 | 10.3 | 11.6 | 16.8 | 27.2
Scenario 2030 | Starlink | Kuiper | Guowang | Qianfan | Others | Total
Low | 12,000 | 1,600 | 800 | 800 | 5,701 | 20,901
Base | 15,000 | 3,236 | 3,000 | 3,000 | 6,639 | 30,875
High | 19,400 | 3,236 | 6,500 | 6,500 | 7,970 | 43,606
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
11 / 17
Notes: Two routes agree. A damped-trend forecast reaches about 36,000 satellites in orbit by 2030; tested on held-back years it erred by 8.6 percent. A bottom-up build from the announced constellations gives 20,901, 30,875 or 43,606 working satellites. The collision-risk index rises to about 17 times the 2014 level in the base case. China's planned shells at 1,050 to 1,200 kilometres are the concern: debris there stays for centuries.

## Slide 12
INFERENCE · HOW SURE ARE WE
Every finding survives an independent check
Finding | Result | Independent check | Verdict
Growth of orbit | 15x active satellites 2014-2026 | UNOOSA registrations track catalogue launches (r = 0.997); UCS 2020 census sits on the same curve | Confirmed
Collision risk | index x10 since 2014 | Same result with 25 km shells and with objects' mean altitude; the densest shell holds mostly working satellites, the second band mostly debris | Confirmed (relative index)
ISR race | China 406 vs India 17 state ISR/military satellites | Name-based lower bound; excluding commercial imagers the ratio stays above 20:1 | Confirmed (lower bound)
Space weather | intense-storm odds x7 at high solar activity | Poisson rate ratio 1.88 per +50 sunspots (p < 0.001); Spearman rho -0.57 | Confirmed
Solar cycle in debris decay | re-entry cycle of 12 years | Found blind by periodogram; matches the ~11-year solar cycle (SILSO maxima) | Confirmed
Forecast to 2030 | ~36k payloads (statistical) vs 31k working (base scenario) | Back-test error 8.6% over 2022-2026; two independent routes agree | Moderate confidence
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
12 / 17
Notes: Before a commander acts, he asks how sure we are. Each headline was checked by a second source or a second method: UN registrations for growth, a second shell size for congestion, a sensitivity test for the intelligence count, two statistical tests for storms, and a back-test for the forecast. The intelligence count is a lower bound: covert satellites would only widen the gap.

## Slide 13
IMPACT · INDIA AND THE ARMED FORCES
India depends on space, but holds less of it
Measure | India | China | USA
Active satellites, Sep 2026 | 78 | 1,531 | 12,959
Active satellites, Jan 2014 (CDM) | 33 | 117 | 502
Military / state-ISR satellites operational | 17 | 406 | 542
Orbital launches in 2025 | 4 | 89 | 172
GEO satellites in the 40-110 E arc (2020) | 24 | 32 | -
Navy
Ocean surveillance rests on radar and AIS satellites; assume carrier groups are tracked.
Air Force
Precision strike needs NavIC and fresh imagery; storms degrade GNSS and HF.
Army
Northern border under persistent ISR (406 Chinese satellites): concealment and deception.
Joint / DSA
ORBITWATCH, SBS-III at pace, manoeuvrable storm-hardened satellites.
Access to space is the bottleneck: China averaged about 16 times India's launch rate over 2021-25.
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
13 / 17
Notes: For India the problem is structural: rising dependence on space for banking, navigation, communications and warning, a falling share of working satellites, and a launch rate far behind China's. For the Services: plan on being watched, and plan on losing some space services in war.

## Slide 14
WARNING · ORBITWATCH
Seven indicators: 6 Red, 1 Amber (Sep 2026)
RED
x10
Collision-risk index, LEO (2014 = 1)
RED
24%
Payloads in orbit, growth per year
RED
43
Chinese state-ISR satellites launched per year (3-yr mean)
RED
0.5%
India's share of active satellites
RED
39%
Intense geomagnetic storm odds per 30 days (sunspot number >= 100, as in 2023-25)
AMBER
1 (2021)
Anti-satellite tests in the last 5 years
RED
162
GEO arc over India: satellites 40-110 E
Each indicator has Amber and Red thresholds and an action on Red, updated from open data.
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
14 / 17
Notes: The study becomes a standing monitor. Seven indicators, each with thresholds and an action on Red. Today six are Red: collision risk, growth rate, Chinese ISR build rate, India's share, storm odds, and crowding of our geostationary arc. The anti-satellite test indicator is Amber.

## Slide 15
WAY FORWARD
Seven actions, each with a lead and a timeline
Action | Lead | When
Stand up ORBITWATCH: weekly space picture and warning matrix | DSA, ISRO NETRA | 4 months
Accelerate SBS-III; buy commercial imagery and radar capacity | DSA, NSIL, industry | 2026-29
Manoeuvre capability, fuel and storm hardening on every new military satellite | DSA, ISRO, DRDO | From 2027
Space-weather cell; drills for degraded GNSS and HF | HQ IDS, IAF Met | 6 months
Rapid reconstitution: SSLV slots and spare satellites on standby | ISRO, NSIL, DSA | 2-3 years
Protect GEO slots and ITU filings in the 40-110 E arc | DoT, ISRO, DSA | Ongoing
Concealment and deception doctrine against persistent ISR | Army, HQ IDS | 12 months
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
15 / 17
Notes: Seven actions from the booklet, each with a lead, a timeline and a measure of success. The first costs almost nothing: the open catalogue and the pipeline already exist. The others build capacity and resilience.

## Slide 16
TECHNICAL SKILLS
Reproducible from raw data to decision
Python pipeline
10 stages, one command, deterministic: two runs give identical results for all headline numbers.
Methods
Change-points, concentration index, kinetic-gas risk index, survival curves, Poisson regression, periodogram, damped-trend forecast with back-test.
Power BI
Star schema: catalogue, 2014 census, storms, fires, calendar, plus the analysis tables; four dashboard pages.
Outputs
Booklet (PDF and Word), this deck, Power BI tables, annotated code.
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
16 / 17
Notes: For the technical criteria: everything is code. One command rebuilds every figure, table and number, and the Power BI dashboard uses the same tables. I can show the dashboard live if the panel wishes.

## Slide 17
The high ground has become a crowd.
DECISION SOUGHT
Approve a four-month ORBITWATCH proof of concept at the Defence Space Agency, using the open catalogue and the pipeline already built. Continue only if it flags at least one actionable conjunction or threat event.
Questions
PROJECT HIGH GROUND · CDM Datathon-2026 · Theme 6.1
17 / 17
Notes: To close: in twelve years orbit became crowded, concentrated and contested, and India's share shrank while its dependence grew. The remedy is numbers, resilience and awareness. The ask is small and time-bound, with a clear stop test. Thank you, sir.